## Slide 1: Dangerous Road Event Detection
Jacob crabtree
Allie jett

## Slide 3: Dataset
Publically available courtesy of Mivia Lab[1]
200 clips of car crashes and car skidding
Approximately 45 minutes of background noise
Audio sampled at 32 kHz and saved as .wav files
Data pre-divided into four completely independent folds
Notes: [1] http://mivia.unisa.it/datasets/audio-analysis/mivia-road-audio-events-data-set/

## Slide 4: Feature Extraction
Loading and cutting wavs
XML description of clips provided
WAVs loaded and cut into clips labeled with class ID
Audio features are extracted from these clips
Example clip

## Slide 5: Feature Extraction
Extracting mfccs
Cut each clip into frames
Tested frame sizes of 50ms, 100ms, and 300ms with 50% overlap
Extracted the 13 lowest Mel-Cepstral Frequency Coefficients for each frame

## Slide 6: Audio “Word” Generation
Treated each frame as being a particular “word”
Used KMeans with various cluster sizes (64, 128, 256, 512, 1024)
  K = number of audio “words” in dictionary
Used KMeans to identify each frame as a word
  Frames with similar MFCCs became essentially equivalent frames

## Slide 7: Bag-of-Words Representation
Used KMeans to effectively generate a dictionary of words
Created a histogram for each clip
  Count of “words”
Low level feature vector of MFCCs became audio words became a histogram
Each audio clip is now treated as a bag of audio words and classified

## Slide 8: Classification
Sk-learn SVC used to classify histograms
Data already split into folds
Used K-folds cross validation using a GridSearchCV to tune kernel, C, and Gamma
  Kernel = ‘rbf’ always outperformed linear
  C is the penalty term
  I forget what gamma is
Tuned parameters per frame length, per KMeans cluster count

## Slide 9: Results
Results for tuning parameters?

## Slide 10: C-VALUES & GAMMA FOR EACH CLUSTER
C-values
Gamma
Chart: 
| 64 | 128 | 256 | 512 | 1024
C-Values | 1 | 2 | 3.5 | 2 | 4.5
Chart: 
| 64 | 128 | 256 | 512 | 1024
Gamma | 0.002 | 0.0012 | 0.0007 | 0.0009 | 0.0005

## Slide 11: Results
After running our test set, we plotted the results of 50ms, 100ms, and 300ms chunked clips together.
The 50ms set did the best, followed by 100ms and then 300ms.
These results were to be expected:
  Smaller chunked segments give a more accurate reading of clustering of “words”.
  Ex: 100 “words” of a “skid” mean less in a 300ms segment than it does a 50ms segment.
Chart: Recognition Rate vs Cluster Sizes
| 64 | 128 | 256 | 512 | 1024
50ms | 0.92 | 0.925 | 0.94 | 0.93 | 0.98
100ms | 0.905 | 0.905 | 0.915 | 0.91 | 0.945
300ms | 0.875 | 0.905 | 0.895 | 0.91 | 0.93

## Slide 12: Future Work
Timing the various methods to see if the accuracy tradeoff is worth having to process less audio
Use of other audio features (such as Bark Sub-bands)
Attempt to classify audio via visual classifications on spectrograms.
Extending this framework to other noises/events (explosion, gunshot, “crime” sounds).

## Slide 13: Comparison to Existing Work
Our work was mostly a replication experiment
Existing work focused more on the implications of a real world set up
  Reducing the db of the .wav file to make it harder to recognize
  Analyzing microphone placement
Our SVM actually outperformed theirs, even with their 0db loss classification
  Maybe we tuned our parameters more than theirs?